## Slide 1: Invertibility Conditions for Floating Point Formulas
Martin Brain
Andrew Reynolds
Cesare Tinelli
Aina Niemetz
Mathias Preiner
Clark Barrett

## Slide 2: SMT Solvers for Quantifiers + Floating Points
Floating point reasoning in SMT is hard
  Bit-blasting [Brillout et al 2009, Brain et al 2019]
  Interval techniques [Brain et al 2014, Marre et al 2017]
Quantified reasoning in SMT is hard
  Heuristic instantiation techniques [deMoura et al 2007]
  Model-based instantiation for finite domains [Wintersteiger et al 2013]
Floating Point + Quantified reasoning in SMT is very hard!
  …no existing works to our knowledge, despite potential applications
    Proving safety properties, synthesizing bounding polynomials, …

## Slide 3: In This Talk:
Towards solving quantified floating points via Invertibility Conditions
  Extends approach for quantified bit-vectors [Niemetz et al CAV 18]
Goal: establish invertibility conditions for theory of floating points
  Developed custom synthesis framework on top of CVC4SY
Preliminary evidence that ICs are useful for solving FP formulas

## Slide 4: What is an invertibility condition?
Given equation :
x. xs~t
  An invertibility condition is a predicate IC(s,t) that holds exactly when the above formula has a solution for x
For example:
  x. x*2=t
   t%2=0 is an invertibility condition for this formula (assuming x,t are integers)

## Slide 5: What can we do with Invertibility Conditions?
Invertibility conditions can be used for:
  Local search techniques [Niemetz et al CAV 2016]
    Accelerate search for satisfiable q.f. inputs
  Solving quantified formulas
    Quantifier elimination
      x. xs~t  IC(s,t)
    Quantifier instantiation
      x. (xs~t  P(x))  (IC(s,t)  P(kIC(s,t)))

## Slide 6: How do we find Invertibility Conditions?
Say I want to find invertibility condition for floating point equation:
  IC. st:FPe,s. (x:FPe,s.xs~t)  I(s,t)

## Slide 7: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FPe,s. (x:FPe,s.xs~t)  IC(s,t)
Can express as a synthesis problem:
…there exists a predicate IC that is equivalent to x:FPe,s.xs~t

## Slide 8: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FPe,s. (x:FPe,s.xs~t)  IC(s,t)
… solve via syntax-guided synthesis (SyGuS) solver CVC4SY ?
?
SY

## Slide 9: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FPe,s. (x:FPe,s.xs~t)  IC(s,t)
Challenge #1: problem is parameteric
  Parameterized by # exponent bits e, # significant bits s

## Slide 10: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5. (x:FP3,5.xs~t)  IC(s,t)
Challenge #1: problem is parameteric
 Solve for a fixed format, check if solution generalizes [Niemetz et al CAV 2018]
  Choose e=3, s=5 … large enough to exhibit FP behaviors, small enough for synthesis to scale

## Slide 11: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5. (x:FP3,5.xs~t)  IC(s,t)

## Slide 12: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5. (x:FP3,5.xs~t)  IC(s,t)
Challenge #2: problem has three levels of quantifier alternation
  …SyGuS solvers only typically handle two

## Slide 13: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5. (x:FP,cs~t )  IC(s,t)
Challenge #2: problem has three levels of quantifier alternation
Expand the innermost quantifier [Niemetz et al CAV 2018]
  Since domain is (relatively) small and finite
    Only 227 values for FP3,5
227

c=1

## Slide 14: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5. (x:FP,cs~t )  IC(s,t)
Challenge #3
227

c=1
…can now give as input to SyGuS solver

## Slide 15: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5. (x:FP,cs~t )  IC(s,t)
Challenge #3: Scalability!
  With respect to BV synthesis @ 4 bits [Niemetz et al CAV 2018]:
    Roughly 14 times more constraints, q.f. FP is much harder than BV
227

c=1
SY

## Slide 16: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5. (x:FP,cs~t )  IC(s,t)
Challenge #3: Scalability
227

c=1

## Slide 17: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5cs,t  IC(s,t)
Challenge #3: Scalability
  Statically compute the I/O behavior of entire domain of IC(s,t)
    Each cs,t is determined by a quantifier-free satisfiability query
      227*227 = 51529, takes ~10 minutes27 = 51529 sat queries to compute for 2-dimensions of FP3,5 time for formats considered in this paper
227 227
 
s=1 t=1
x.x*s=t? where s, t are constants

## Slide 18: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5cs,t  IC(s,t)
227 227
 
s=1 t=1

## Slide 19: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5cs,t  IC(s,t)
227 227
 
s=1 t=1
SY
c1,2  IC(1,2)
c3,7  IC(3,7)
c1,7  IC(1,7)
…
Sample
Candidate Solutions

## Slide 20: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5cs,t  IC(s,t)
227 227
 
s=1 t=1
SY
c1,2  IC(1,2)
c3,7  IC(3,7)
c1,7  IC(1,7)
…
Sample
Candidate Solutions
Test (Fast!)

## Slide 21: How do we find Invertibility Conditions?
Can express as a synthesis problem:
  IC. st:FP3,5cs,t  IC(s,t)
227 227
 
s=1 t=1
SY
c1,2  IC(1,2)
c3,7  IC(3,7)
c1,7  IC(1,7)
…
Sample
Candidate Solutions
“User in the loop”

## Slide 22: Visualizing I/O Specs of Invertibility Conditions
White = IC is true, Black = IC is false
   Behavior of IC is highly complex!
sub-normal t
normal t
t=0
t=
t=NaN
s
t
Can express as a synthesis problem:
  IC. st:FP3,5cs,t  IC(s,t)
227 227
 
s=1 t=1

## Slide 23: Synthesizing Invertibility Conditions
SY

## Slide 24: Synthesizing Invertibility Conditions
SY
“Full I/O Specification for IC”
(Verifier)
(Synthesizer)

## Slide 25: Synthesizing Invertibility Conditions
SY
Initial Examples
C
Red = Counterexample not specified

## Slide 26: Synthesizing Invertibility Conditions
SY
IC1(s,t)

## Slide 27: Synthesizing Invertibility Conditions
SY
Test
Counterexamples
C,C1

## Slide 28: Synthesizing Invertibility Conditions
SY
Counterexamples
C,C1,C2
IC2(s,t)

## Slide 29: Synthesizing Invertibility Conditions
SY
Counterexamples
C,C1,C2,C3
IC3(s,t)

## Slide 30: Synthesizing Invertibility Conditions
SY
Counterexamples
C,C1,C2,C3,C4
IC4(s,t)

## Slide 31: Synthesizing Invertibility Conditions
SY
Counterexamples
C,C1,C2,C3,C4,C5
IC5(s,t)

## Slide 32: Synthesizing Invertibility Conditions
SY
Counterexamples
C,C1,C2,C3,C4,C5,C6

## Slide 33: Synthesizing Invertibility Conditions
SY
Counterexamples
C,C1,C2,C3,C4,C5,C6

## Slide 34: Synthesizing Invertibility Conditions
?
SY
Counterexamples
{ C | s.t. SC}
IC(s,t)G
User may control:
Grammar G for synthesizer
“Side condition” SC for verifier

## Slide 35: Finding Invertibility Conditions: Results
In total, found 167 of 188 conditions

## Slide 36: Finding Invertibility Conditions: Results
In total, found 167 of 188 conditions
  14 choices for argument positions of 
    add1, sub1,2, mult1, div1,2, rem1,2, fma1,3, sqrt1, abs1, neg1, roundToIntegral1
  13 choices for ~
    =, , , >, <, , isNormal, isSubnormal, isZero, isInfinite, isNaN, isPositive, isNegative
  7 additional ICs for equations with only a relation, e.g. x>t
   14*13 + 7 = 188
    When applicable, ICs hold for each 5 rounding modes {RNE, RNA, RTP, RTN, RTZ} of operator
xs~t

## Slide 37: Finding Invertibility Conditions: Results
In total, found 167 of 188 conditions

## Slide 38: Finding Invertibility Conditions: Results
???
…behavior is pseudo-random!
Others were hard to find

## Slide 39: Do Invertibility Conditions hold for all FP Formats?
We checked all 167 invertibility conditions on other FP Formats
  Targeted formats FP3,5, FP4,5, FP4,6, FP5,11, FP8,24, FP11,53
  All invertibility conditions (appear to) generalize to all formats
    Successful in 94.5% of the above cases using CVC4, Z3 (failures due to timeouts)
    Approximately 32 days of compute time
Future work: Format-Independent Verification!

## Slide 40: What can we do with Invertibility Conditions?
Floating point invertibility conditions can be used for:
   In this paper: Quantifier Elimination
    Currently limited to “linear” (single variable) quantified floating points
    Preliminary work in this paper:
      Implemented prototype preprocessing pass in CVC4 leveraging ICs
        Led to +7 / 56 quantified FP verification benchmarks from SMT LIB

## Slide 41: What can we do with Invertibility Conditions?
Summary of intuition:

## Slide 42: What can we do with Invertibility Conditions?
Summary of intuition:
Try inverse in rounding mode R?

## Slide 43: What can we do with Invertibility Conditions?
Summary of intuition:
…
…
red = wrong (showing R=RNE)
Try inverse in rounding mode R?

## Slide 44: What can we do with Invertibility Conditions?
Summary of intuition:

## Slide 45: What can we do with Invertibility Conditions?
Summary of intuition:


## Slide 46: What can we do with Invertibility Conditions?
Summary of intuition:

Try rounding towards positive

## Slide 47: What can we do with Invertibility Conditions?
Summary of intuition:

Try rounding towards positive
Try rounding towards negative

## Slide 48: What can we do with Invertibility Conditions?
Summary of intuition:

Try rounding towards positive
Try rounding towards negative
Corner case, try zero

## Slide 49: What can we do with Invertibility Conditions?
Similar intuition for many other invertibility conditions:
      Equation Set of Possible Solutions
corner cases for
0, , NaN
+

## Slide 50: Ongoing Work
Integrate invertibility conditions into quantifier instantiation in CVC4
Format-independent verification of invertibility conditions
  “Towards Bit-Width Independent Proofs in SMT Solvers” [Niemetz et al CADE 2019]
Tackle harder synthesis problems using our synthesis framework:
  Equations that are “non-linear”, e.g. x*x=t
  Invertibility conditions that have 3+ dimensions
    ...

## Slide 51: Ongoing Work
FP equations having 3+ dimensions
  Fused multiply-add with equality
Thanks for Listening!
: time